## Slide 1: Gate Level Minimization
Course Teacher: Md. Hamjajul Ashmafee
Lecturer, CSE, IUT
Email: ashmafee@iut-dhaka.edu
CSE 4205 Digital Logic Design

## Slide 2: Remaining to Add
Review other books and internet resources
Notes: What is digital computer? Examples where we can use this thing.

## Slide 3: To be noted more:
Circuit diagrams of NAND and NOR implementation
3.7 – other two level implementation
Is XNOR satisfies associative law?? – even function??
  Slide 52 (Few important points)
Quine McClusky method/ tabular method
  Takes notes shortly from book
  Draw the figures clearly

## Slide 4: Introduction
Gate level minimization
  A design task to get optimized digital circuit
  But difficult for manual approach when the number of inputs are many
  Contemporary computer applications can easily minimize it efficiently
    So, we need to understand the underlying mathematical description

## Slide 5: Implementation of Boolean Function
Complexity of implementing digital logic gates of any Boolean function depends on the complexity of its algebraic expression.
  A Boolean function can be expressed in different ways, but their truth table representation is unique
  This Boolean expression can be simplified by Boolean algebra (Cut-and-try method)
    But it’s manual and there’s no specific rules to proceed next step
Map method or Veitch/Karnaugh Map or K-map
  Simple and straightforward procedure to minimize Boolean function
  Also be regarded as pictorial form of a truth table

## Slide 6: The Map Method – K-map
K-map is made of squares
  Each square represents a minterm of the function
Graphical representation of a Boolean function in the map enclosing those squares whose minterms are included in the function
  This representation reveals all possible ways a function may be expressed in standard form (SOP or POS)
    A designer should identify various patterns to derive alternative simplified algebraic expression
      A super optimized expression contains minimum number of terms and with smallest possible number of literals in each term
      But sometimes more than one expressions may satisfy this minimization criteria – all of them are correct
Notes: Target:
Make the group of 1s which are adjacent by edge and maintain the count as 2n
Cover all the minterms at least once [more than one might cause redundant terms in the simplified expression]
Try to make the group larger to get shorter expression [as expected]
  To do this if it requires to repeat a covered minterm, it is acceptable.

## Slide 7: Two-Variable K-map
Two variables – Four minterms
  Four Squares in K-map
  Another way to represent any of the 16 functions of two variables
  Minterm corresponding to a square can be obtained from the concatenation of the row and column number
Note: A square is marked with 1, if that minterm asserts the function
Notes: AND operation
xy = already in minterms
OR operation
x+y = it is not in canonical form – must be converted considering all possible minterms
= x(y+y’) + y(x+x’)

## Slide 8: Three-Variable K-Map
Three variables – Eight minterms
  Eight squares in k-map
Minterms are expressed symbolically in binary equivalent sequence but arranged in k-map as a sequence of reflected code
  Only one-bit changes in value from one adjacent column to the next
  Any two adjacent squares in the map differ by only one variable
  Basic property of K-map
Notes: In four squares, each variable is 1 (expressed as unprimed)
In other four squares, each variable is 0 (expressed as primed)

## Slide 9: Three-Variable K-Map: Simplification
If any two adjacent squares (vertically or horizontally) are considered as sum of them, those two minterms could be simplified to a single product term following the postulates of Boolean algebra ().
    Dissimilar variable will be removed
    Example: m5 and m7
  Note: Two squares are adjacent even though they don’t touch each other
    Like world map
    Example: m0 and m2
Notes: Verification: (Just like a rolled paper)
m0 +m2 = ?
m4 +m6 = ?

## Slide 10: 3-variable K-Map: Example
Notes: Answer:
Answer:
𝑥’𝑦 +𝑥𝑦’
𝑦𝑧 +𝑥𝑧’

## Slide 11: 3-variable K-Map: Example…
Solve these ?
Note:
Like this, 4 adjacent squares are also possible following same postulates of Boolean algebra
Use of squares more than once (repeatedly) makes a term more minimized
If the function is not expressed in canonical form, missing minterms should be obtained
Minimized function must be expressed in standard form
Notes: = m0 + m2 + m4 + m6 = ? ()
Answer:
= m0 + m2 + m4 + m6 = ? (𝐀𝐧𝐬𝐰𝐞𝐫: 𝒛’)
𝑭 = 𝒛’ + 𝒙𝒚’

## Slide 12: 4-Variable K-Map
4 variables – 16 minterms
  16 squares in K-map
Both columns and rows are numbered in Gray code sequence
  Only one variable change in any two adjacent squares row-wise or column-wise
The map is considered on the surface whose top and bottom edges and right and left edges are attached to each other to form adjacent squares
Notes: Verification: (Just like a rolled paper)
m0 +m2 = ?
m3 +m11 = ?

## Slide 13: 4-Variable K-Map: Representation
Notes: Show how to calculate the minterm number.

## Slide 14: 4-Variable K-Map: Example
Solve this:
Notes: Answer:
Answer:
𝑦^′+𝑤^′ 𝑧^′+𝑥𝑧^′
𝐵^′ 𝐷^′+𝐵^′ 𝐶^′+𝐴′𝐶𝐷′

## Slide 15: Basic Definition: Implicant
Implicant is a group of adjacent squares in K-map consisting of 2n 1s representing true minterms in the function
    Alternatively, Implicant is a product term (or minterm) of any function so that it implies the function (i.e., if the implicant is true, the function will be true)
A prime implicant is a product term obtained by combining the maximum possible number of adjacent squares in the map.
    Where, this number satisfies 2n
    A single square itself represents a prime implicant if it has no other adjacent 1’s square
Essential prime implicant, is that prime implicant that has at least one minterm which is not covered by any other prime implicants.
    This prime implicant must be included in the simplified expression
Notes: To minimize the function:
  We must cover all minterms that asserts the function
  Number of the terms in the simplified expression must be minimum
  No redundant term should be in minimized expression. (i.e., all the minterms of a group are already covered by other group)
There may have more than one expressions those satisfy these criteria

## Slide 16: Basic Definition: Implicant – Example
2. There are more alternatives of prime
implicants to cover remaining minterms
1. The essential prime implicants are the
only ways to cover some minterms
Notes: To minimize the function:
  We must cover all minterms that asserts the function
  Number of the terms in the simplified expression must be minimum
  No redundant term should be in minimized expression. (i.e., all the minterms of a group are already covered by other group)
There may have more than one expressions those satisfy these criteria

## Slide 17: Implicants in 3- and 4-variable K-map
3 variable K-map
  One square – a term with three variables
    One minterm itself
  Two adjacent squares – a term with two variables
  Four adjacent squares – a term with one variable
  Eight adjacent squares – always 1
    Constant function
4 variable K-map
  One square – a term with four variables
    One minterm itself
  Two adjacent squares – a term with three variables
  Four adjacent squares – a term with two variables
  Eight adjacent squares – a term with three variables
  Sixteen adjacent squares – always 1
    Constant function

## Slide 18: 5- and 6-Variable K-Map
DEF
ABC
6-variable K-map
Notes: Show how m18 and m50 are adjacent
Maps with 5 or more variables are not simple to manage as the number of minterms in such maps is 32 or more and a complex geometry is involved to find out adjacent squares

## Slide 19: POS & SOP Simplification
SOP simplification – so far, we have minimized the previous Boolean functions
    With minor modification, POS simplification is also achievable
Procedure:
  Mark the empty squares by 0’s in the K-map for any Boolean function
  Combine them into valid adjacent squares
    A simplified SOP expression of the complement of the function (i.e., ) is achieved
  The complement of gives back the function in simplified POS form following the De Morgan’s law

## Slide 20: POS & SOP Simplification - Example
  Simplification in SOP and POS form
SOP:
POS:

## Slide 21: POS & SOP Simplification – Gate Level Implementation
  Gate level implementation of simplified SOP and POS expressions
Notes: It is assumed that input variables are also available in their complement directly
Implementation of standard form is said to be a two-level implementation
  But sometimes two-level implementation is impractical if the number of inputs are so many (more than hundreds or thousands)

## Slide 22: POS & SOP Simplification – Important
If the function is expressed in canonical form using maxterms (POS), the simplified expression is also derivable if we consider those minterms in K-map marking with 0’s
    Then we can account those remaining squares to get the simplified SOP expression of F
    Otherwise, we can consider the currently marked squares with 0s to get the simplified SOP expression of F’
If any expression is expressed in standard POS format, we have to use the complement of that function to get its correspondent expression of F’ in standard SOP format
    Example:
      Then, will be obtained to calculate all the minterms causes 0.

## Slide 23: Incompletely Specified Functions Don’t Care Conditions
Fact: Logical sum of minterms (i.e., ) of a Boolean function specifies the condition under which the function is true (logic 1)
    The function is false (logic 0) for rest of the minterms
This pair of conditions assumes that all possible combinations for the variables are valid for the function (either logic 0 or logic 1)
    But in practice, some combinations of variables may not be valid for a Boolean function in some applications
    Example: BCD – a 4-bit binary code for decimal digits
      There are six such combinations which are not used and considered as unspecified
Incompletely Specified Functions
    Functions those have unspecified outputs for some input combinations
    We simply don’t care what value will be produced by the function for those unspecified minterms
    Those unspecified minterms of any function are called don’t care conditions
      Useful for further simplification of any Boolean expression
Notes: Unspecified minterms – minterms which are not of our interest rather ignore when they are produced

## Slide 24: Don’t Care Conditions
A don’t care minterm is a combination of variables whose logical value (0 or 1) is not specified (i.e., defined) in the Boolean function
    So that corresponding square can’t be marked with 1 or 0 in the K-map
    Rather “X” could be placed in that corresponding square distinguishing from 0 and 1
    It indicates that we don’t care whether the value of 0 or 1 is assigned to that function for that minterm
For better simplification, adjacent don’t care square may be assumed to be either 0 or 1
    Preference of 0 or 1 depends on which combination gives the simplest expression
Trick: To get the simplified expression of any Boolean function, we must include all 1s, but we may or may not include any of the Xs based on preference
    Initially, those don’t care minterms could be unspecified, but when a particular choice is made, they should be treated differently.
Notes: Note: When a don’t care minterm is selected as a true minterm, that should be treated as 1 and then other don’t care minterms should be treated as false minterm

## Slide 25: Don’t Care Conditions – Example
Note: It is also possible to simplify in POS form using its complement. i.e.,
Notes: Though these two functions are not algebraically equal, both of them cover all specified minterms.
  In the first choice, minterm 0 and 2 are treated logic-1 and minterm 5 is treated logic-0
  In the second choice, minterm 5 is treated logic-1 and minterm 0 and 2 are treated logic-0
As we are considering this incompletely specified function, the only difference between these two functions are in don’t care minterms

## Slide 26: NAND & NOR implementation
Digital circuits are frequently constructed with NAND or NOR gates rather than AND, OR and NOT gate because:
    These gates are easier to fabricate with electronic components
    They are used as basic gates in all ICs
    Any logic circuits can be implemented with these gates
      So, they are called universal gates
Because of prominence of these gates, some rules and procedures have been developed to convert any circuit using AND, OR and NOT gates into equivalent circuit using NAND or NOR gates

## Slide 27: NAND implementation
To show that any function can be implemented with NAND gate, we need only to show AND, OR and NOT gates obtained with NAND gates alone
Note: One-input NAND gate behaves exactly like an inverter.
Notes: A convenient way to implement a Boolean function with NAND gates is to obtain the simplified Boolean function in terms of Boolean operators (i.e., AND, OR, NOT) and then convert the function to NAND logic
All inputs of any gate (for any multi-input gate) are merged together to generate one input gate – like inverter

## Slide 28: NAND Implementation: Graphic Symbols
To facilitate the conversion to NAND logic, it is convenient to define an alternative graphic symbol for the NAND gate
    AND-invert: Consists of an AND gate followed by a small bubble (i.e., complement)
    Invert-OR: Consists of an OR gate preceded by a bubble in each input (i.e., complements each input)
  Both of them are equal because of De Morgan's theorem
  Useful for analysis and design NAND circuits

## Slide 29: Two Level NAND Implementation
For two level NAND implementation, initially the function must be simplified in SOP form
    AND gate will be replaced by AND-invert NAND gate in the first level and OR gate will be replaced by invert-OR NAND gate in the second level
      As Bubble denotes complementation, two cascaded bubbles will be cancelled by each other
    But, if there is a single-variable term in first level of implementation, an inverter will be required for that term
      We can replace that inverter changing the input variable into its complement (i.e., x will be x’ in the input)

## Slide 30: Two Level NAND Implementation: Procedure
Simplify the function and express it in SOP form
To implement the first level gates, all product terms of the expression (having at least two variables) drawn with NAND gates
    Inputs of these NAND gates will be the same literals of the previous terms
Draw another single NAND gate (representing invert-OR) in the second level with inputs coming from outputs of the first level gates
A term having a single-variable term requires an inverter in the first level. However, if that variable is complemented, it can be connected directly to the input of the second level NAND gate

## Slide 31: Two Level NAND Implementation - Example
Example:
  The NAND implementation can be verified algebraically using De Morgan’s law
    Verification:
Solve this:
Notes: Answer:
Answer: 𝐹=𝑥𝑦^′+𝑥^′ 𝑦+𝑧

## Slide 32: NOR implementation
NOR operation is the dual of NAND operation
  All procedures and rules for NOR logic are the dual of the corresponding procedures and rules developed for NAND logic
Another universal gate to implement any logic circuit

## Slide 33: NOR implementation
To show that any function can be implemented with NOR gate, we need only to show that AND, OR and NOT gates obtained with NOR gates alone
Note: One-input NOR gate behaves exactly like an inverter.
Notes: A convenient way to implement a Boolean function with NOR gates is to obtain the simplified Boolean function in terms of basic Boolean operators and then convert the function to NOR logic

## Slide 34: NOR Implementation: Graphic Symbols
To facilitate the conversion to NOR logic, it is convenient to define an alternative graphic symbol for the NOR gate
    OR-invert: Consists of an OR gate followed by a small bubble (i.e., complement)
    Invert-AND: Consists of an AND gate preceded by a bubble in each input (i.e., complements each input)
  Both of them are equal because of De Morgan's theorem
  Useful for analysis and design NOR circuits

## Slide 35: Two Level NOR Implementation
For two level NOR implementation, initially the function must be simplified in POS form
  Note: Simplified POS expression can be obtained by combining all 0s and complementing that expression
    OR gate will be replaced by OR-invert NOR gate in the first level and AND gate will be replaced by invert-AND NOR gate in second level
      As Bubble denotes complementation, two cascaded bubbles will be cancelled by each other
    But, if there is a single-variable term in first level of implementation, an inverter will be required for that term
      We can replace that inverter changing the input variable into its complement (i.e., x will be x’ in the input)

## Slide 36: Two Level NOR Implementation: Procedure
Simplify the function and express it in POS form
To implement the first level gates, all sum terms of the expression (having at least two variables) drawn with NOR gates
    Inputs of these NOR gates will be the same literals of the previous terms
Draw another single NOR gate (representing invert-AND) in the second level with inputs coming from outputs of the first level gates
A term having a single variable requires an inverter in the first level. However, if that variable is complemented, it can be connected directly to the input of the second level NOR gate

## Slide 37: Two Level NOR Implementation - Example
Example:
  The NOR implementation can be verified algebraically using De Morgan’s law
    Verification:

## Slide 38: Multiple Level NAND Implementation
Standard form in SOP or POS expression can be implemented in a two-level implementation
  But sometimes, three or more level getting structure are also observed in digital systems
There are two approaches to design a multi-level NAND circuits:
  Express the Boolean function in terms of AND, OR and NOT operators
  Two alternative ways:
    Approach 1: All the AND, OR and NOT gates would be converted to its corresponding NAND representation
    Approach 2: Convert each AND to AND-invert and each OR to Invert-OR gates
  There should have two cascaded bubbles or inverters who will cancel each other
      Otherwise, one extra inverter should be inserted, or input variables should be complemented

## Slide 39: Multiple Level NAND Implementation: Example
Example 1:
    We could simplify this expression to its SOP form, but here a multilevel NAND circuit is preferred
Approach 1

## Slide 40: Multiple Level NAND Implementation: Example
Example 1:
    We could simplify this expression to its SOP form, but here a multilevel NAND circuit is preferred
Approach 2

## Slide 41: Multiple Level NAND Implementation: Example…
Example 2:
    We could simplify this expression to its SOP form, but here a multilevel NAND circuit is preferred
Approach 1

## Slide 42: Multiple Level NAND Implementation: Example…
Example 2:
    We could simplify this expression to its SOP form, but here a multilevel NAND circuit is preferred
Approach 2

## Slide 43: Multiple Level NOR Implementation
There are two approaches to design a multi level NOR circuits:
  Express the Boolean function in terms of AND, OR and NOT operators
  Two alternative ways:
    Approach 1: All the AND, OR and NOT gates would be converted to its corresponding NOR representation
    Approach 2: Convert each AND to invert-AND and each OR to OR-invert gates
  There should have two cascaded bubbles or inverters who will cancel each other
      Otherwise, one extra inverter should be inserted, or input variables should be complemented

## Slide 44: Multiple Level NOR Implementation- Example
Example 1:
    We could simplify this expression to its POS/SOP form, but here a multilevel NOR circuit is preferred
Approach 1

## Slide 45: Multiple Level NOR Implementation- Example…
Example 1:
    We could simplify this expression to its POS/SOP form, but here a multilevel NOR circuit is preferred
Approach 2

## Slide 46: Exclusive-OR Function
Exclusive-OR (XOR) symbolized as
    Example:
It performs the Boolean operation:
  The XOR function is 1 if only x is 1 or only y is 1 – x and y are differed in value
    So, it is called difference function
    For multiple variables, XOR is 1 if the total number of 1s in the input is odd.
For XOR operation, following statements are true:
Notes: These statements also could be verified with truth table
x⊕𝑦^′=𝑥^′⊕𝑦=xy+x^′ y^′=(x⊕𝑦)′
These statements also could be verified with truth table

## Slide 47: Exclusive-NOR Function
Exclusive-NOR (XNOR) symbolized as
    Example:
It performs the Boolean operation:
  By definition, XNOR function is the complement of the XOR i.e.
  The XNOR function is 1 when both x and y are 1 or both of them are 0
    So, it is known as equivalence function considering two variables gate
    For multiple input, XNOR is 1 if the total number of 1s in the input is even

## Slide 48: XOR an XNOR Function…
Exclusive-OR (XOR) operation is both commutative and associative:
Exclusive-NOR (XNOR) operation is also both commutative and associative:
So, the two inputs of XOR (or XNOR) gate can be interchanged without affecting the operation
Also, we can evaluate a three or more inputs XOR (or XNOR) gate in any order
  No need to include parentheses for further clarification
  But multiple input XOR and XNOR gates are very difficult to fabricate with hardware
Notes: Even two input XOR and XNOR gate are constructed with other types of gates (i.e., AND, OR, NOT, NAND,…)
x⊕𝑦^′=𝑥^′⊕𝑦=xy+x^′ y^′=(x⊕𝑦)′
These statements also could be verified with truth table

## Slide 49: Implementation of XOR Gate
Notes: Even two input XOR and XNOR gate are constructed with other types of gates (i.e., AND, OR, NOT, NAND,…)
Verify these circuit diagrams for better understanding

## Slide 50: Implementation of XNOR Gate
XNOR gate with AND-OR-NOT gates
XNOR gate with NAND gates
Notes: Even two input XOR and XNOR gate are constructed with other types of gates (i.e. AND, OR, NOT, NAND,…)
Verify these circuit diagrams for better understanding

## Slide 51: Usage of XOR and XNOR Gates
Only a limited number of Boolean functions can be expressed with XOR and XNOR gates
In some digital system designs, they could be used
  Specially, they are useful in -
    Arithmetic operations (e.g., add, subtract, etc.)
    Logical operation (e.g., complement)
    Error detection and correction (e.g., parity generator and checker)
    Gray code conversion
XOR gate is used extensively, XNOR could be implemented as XOR-inverter.

## Slide 52: Odd Function with XOR gate Considering Logic-1
Basically, two input XOR gate could be defined as difference function
  But, if we increase the number of input to three or more, definition will be changed
    Example:
  Here, three input XOR gate produces 1 if only one variable is 1 or all three variables are 1
Definition: A multiple input XOR gate operates as an odd function i.e. an odd number of inputs should be 1.
    An n–variable XOR function is an odd function defined as the logical sum of the 2n/2 minterms whose binary numerical values have an odd number of 1s
Notes: So, to obtain even function considering logic-1, we need to use same XOR gate configuration with additional NOT gate at the end (i.e. complementing that XOR configuration = ()
  So last level XOR gate (output XOR gate) could be replaced with an XNOR gate. (Draw the diagram including an inverter with the above figure)
  Here, the even function considering logic-1 will be 1 when an even number of its variables are 1 including that combination as well which has no variable equals 1.
  An n–variable even function could be defined as the logical sum of the 2n/2 minterms whose binary numerical values have an even number of 1s
So, to obtain even function considering logic-1, we need to use same XOR gate configuration with additional NOT gate at the end (i.e. complementing that XOR configuration = (𝐴⊕𝐵⊕𝐶)′=∑(0,3,5,6) )
  So last level XOR gate (output XOR gate) could be replaced with an XNOR gate. (Draw the diagram including an inverter with the above figure)
  Here, the even function considering logic-1 will be 1 when an even number of its variables are 1 including that combination as well which has no variable equals 1.
  An n–variable even function could be defined as the logical sum of the 2n/2 minterms whose binary numerical values have an even number of 1s

## Slide 53: Odd and Even Function with Four Variables Considering Logic-1
Algebraic expression of odd function with 4 variables:
Algebraic expression of even function with 4 variables:
  (

## Slide 54: Few Important Points***
For same odd number of variables, the XOR and XNOR function will produce same truth table
For same even number of variables, the XOR and XNOR function will produce opposite (complementary) truth table
Notes: Here only “two input gate” system is considered

## Slide 55: Application: Parity Generator and Checker
XOR function is very useful for error detection and correction codes
Parity bit is an extra bit which is usually included with original message during transmission for error detection
  Parity Generator – the circuit that generates the parity bit in the transmitter
  Parity Checker – the circuit that checks the parity in the receiver
Example:
  Consider a three bit message (e.g. x, y, z) to be transmitted together with an even parity bit (e.g. P)

## Slide 56: Parity Generator Circuit
In this circuit, three bits (i.e. x, y, z) in the message are inputs and even parity bit (i.e. P) is the output
  For even parity, the bit P must be produced to make the total number of 1s (including P) even.
  So, P makes an odd function, i.e.

## Slide 57: Parity Checker Circuit
In this circuit, four bits (i.e. x, y, z and P) in the transmitted message are inputs and error checker bit (i.e. C) is the output
  For even parity checking, the checker bit C is 1 if an error occurs, i.e. if the total number of 1s in the received message is odd.
  So, C makes another odd function, i.e.
Notes: This same circuit could be used as parity bit (P) generator if the input P in that circuit made ground (0) [to keep the z intact] and denote the output as C

## Slide 58: Prime Implicants Selections

## Slide 59: Prime Implicants Selections

## Slide 60: The Tabular Method / Quine-McCluskey Method

## Slide 61: The Tabular Method (Alternative Way)
(difference)
(old diff, new diff)

## Slide 62: The Tabular Method
Verification using K-map:

## Slide 63: Prime Implicants Determination
Another Example:

## Slide 64: Prime Implicants Selections

## Slide 65: The Tabular Method
Verification using K-map:

## Slide 68: Administration

## Slide 69: Administration

## Slide 70: Administration

## Slide 71: Administration

## Slide 72: Administration

## Slide 73: Administration

## Slide 74: Administration