## Slide 1: Combinational Logic with MSI & LSI
Course Teacher: Md. Hamjajul Ashmafee
Lecturer, CSE, IUT
Email: ashmafee@iut-dhaka.edu
CSE 4205 Digital Logic Design

## Slide 2: Remaining to Add
Review other books and online resources
Notes: What is digital computer? Examples where we can use this thing.

## Slide 3: Review
We have already learned about
  Binary numbers and Binary codes are representation of discrete quantities of information.
  These binary variables (signals) are applied by electric voltages or some other means.
  This signal can be manipulated through different digital logic gates to perform required functions.
  Boolean algebra is used to express and manipulate the Boolean functions
  Several methods (K-map, tabular method,…) can be used to simplify the Boolean functions and optimize the gate implementations
In this chapter, we will learn how to formulate various systematic design and analysis the procedures of combinational circuits.
Notes: We will learn to perform two tasks:
Analyze the behavior of the given logic circuit
Synthesize (build) a circuit which will endorse that behavior
Extra: write a HDL code to model the combinational circuit
We will introduce some most important standard combinational circuits which are commonly used in higher level digital system design as well
They are available as ICs
Also known as MSI circuits which are unit standard cells for VLSI
This design procedure is called hierarchical design where creation of higher level circuits depends on lower level circuits which are already produced

## Slide 4: Introduction
Logic circuits of any digital system may be any of:
    Combinational Logic Circuit
    Sequential Logic Circuit
A combinational circuit is the circuit whose outputs at any time are determined directly from the present combination of inputs without regarding to previous inputs or outputs.
    Operation of any combinational circuit can be specified by a set of Boolean functions
On the other hand, Sequential circuits employ memory elements (binary memory cells) in addition to the logic gates.
    Their outputs are the function of the present inputs and the state of the memory elements.
    Its behavior must be specified by a time sequence of inputs and internal states of memory.

## Slide 5: Combinational Circuit
Combinational circuits consists of interconnection of logic gates
    Logic gates react to the values of the signal at the inputs and produce required output based on the definition
    These input and output signal exists physically as analog signal which must be interpreted as a binary signal representing either logic-1 or logic-0
But, In many application, the source and destination of the combination circuit are storage registers
    If the registers are included with the combinational circuit, then total circuit must be considered as a sequential circuit
Note: A sequential circuit is circuit which has logic gates with feedback path or memory elements
    A feedback path is a connection from output of any logic gate partially forms an input to any previous gate

## Slide 6: Combinational Circuit: Block Diagram
Block diagram of a combinational circuit with n input and m output binary variables:
For n input variables, there are 2n possible combinations of the binary inputs (from external sources)
  For each input combination, there is one possible value for each output variable (to external destinations)
A combinational circuit can be specified as a truth table that enlists output values for each input combination
  It is also specified as a Boolean function expressed in terms of the n input variables

## Slide 7: Combinational and Sequential Circuit

## Slide 8: Analysis of a Combinational Circuit
Analysis of any combinational circuit starts with a logic diagram
  Finally we will determine the function that the circuit implements, generates the truth table and feasibly explains the operation of the circuit.
  If the function name or its explanation are already mentioned with logic circuit, then we need to verify it (verification)
  Another way to analyze any circuit with logic simulation if the number of inputs is very large

## Slide 9: Analysis Procedure: To Obtain Boolean Function
Make sure that the given circuit is a combinational circuit, not sequential
To obtain Boolean function:
    Label all the gate outputs that are the function of input variables with arbitrary symbols
      Determine those functions
    Also label the intermediate gate outputs that are the function of any input variables or previously defined symbols (i.e. already labeled gate outputs)
      Find those functions as well
    Repeat the process of step (b) until the output of the logic circuit is obtained
    By repeated substation of previously defined intermediate functions, obtain the output Boolean function in terms of input variables
Notes: The success of an investigation/analysis such circuit is enhanced, if one has previous experience and familiarity with a variety of digital circuits

## Slide 10: AP: To Obtain a Boolean Function – Example Given Logic Circuit
Notes: The success of an investigation/analysis such circuit is enhanced, if one has previous experience and familiarity with a variety of digital circuits

## Slide 11: AP: To Obtain a Boolean Function – Example… Following procedure
Step (a):
Step (b and c):
Step (d):
F1
Notes: The success of an investigation/analysis such circuit is enhanced, if one has previous experience and familiarity with a variety of digital circuits

## Slide 12: Analysis Procedure: To Obtain Truth Table
Make sure that the given circuit is a combinational circuit, not sequential
To obtain the truth table from the logic diagram directly:
    Determine the number of input variables in the circuit
      For n inputs, form the 2n possible input combinations and list them as binary number from 0 to (2n-1)
    Label the intermediate gate outputs that are the function of any input variables or previously labeled gate outputs
    Obtain the truth table for those intermediate outputs
    Proceed to obtain for the outputs of those gates which are the function of previously defined values until the columns for all outputs are determined
Otherwise, from the derived function, it can be obtained very easily
Notes: The success of an investigation/analysis such circuit is enhanced, if one has previous experience and familiarity with a variety of digital circuits

## Slide 13: AP: To Obtain Truth Table - Example
Note: This truth table is identical to the truth table of the full adder
Notes: The success of an investigation/analysis such circuit is enhanced, if one has previous experience and familiarity with a variety of digital circuits

## Slide 14: Design of Any Combinational Circuit
Design of a combinational circuit starts from a problem statement (design objective)
  And it ends in a logic circuit diagram or a set of Boolean functions from where the logic diagram can be obtained.
There are some steps to be followed to achieve the requested combinational circuit

## Slide 15: Design Procedure
From the specification of the circuit, determine the required number of inputs and outputs
      Assign a symbol to each input and output variables
Derive the truth table from the specification that defines the required relationship between inputs and outputs
      Input columns have 2n different combinations for n input variables
      Output values are determined from the problem statement
      The specifications may indicate that some input combinations will not occur – don’t care conditions
Obtain the simplified Boolean functions for each output as a function of the input variables
      These output functions gives the exact definition of the circuit
      These output functions should be simplified by any simplification method like k-map, tabular method, algebraic manipulation
Draw the logic diagram and verify the correctness of the design
Notes: It is important that the problem statement is interpreted correctly in the truth table, otherwise for any kind of incompleteness, it may result in an incorrect truth table.
A logic diagram is useful to visualize the gate implementation of the expression

## Slide 16: Design Procedure: Considerations
In a particular application, certain criteria will serve as a guide to choose an implementation among different alternatives
A practical design method considers such constraints:
    Minimum number of gates
    Minimum number of inputs to a gate
    Minimum propagation time of the signal through the circuit
    Minimum number of interconnections
    Limitations of the driving capabilities of each gate (i.e. the number of gates to which this output may be connected)
  Based on the application, those constraints will be prioritized.
  So there is no general statement to constitute an acceptable implementation

## Slide 17: Design Procedure: Considerations…
Most of the cases, the implementation begins with producing the simplified Boolean functions in standard form
  It may proceed to further steps to meet other performance criteria

## Slide 18: Design Procedure: Example
Circuit specification:
  In practical different digital systems may use different codes and they may need to exchange information
  So a code converter circuit is required between them to make these two systems compatible even though they uses different binary codes
Initial Consideration:
  To convert from binary code A to binary code B, the input lines must have the bit combinations specified by code A
    The output lines must generate the corresponding bit combinations specified by code B
    Now we have to design this combinational circuit assuming code A as BCD and code B as excess-3 for decimal digits

## Slide 19: Design Procedure: Example…
Truth Table for 4 input and 4 output variables:
Notes: Six combinations are not listed in this truth table are don’t care combinations
  These values have no meaning in BCD and they will never occur in actual operation of the circuit

## Slide 20: Design Procedure: Example…
K-map for 4 output variables to obtain their simplified Boolean functions:
Notes: Here 1s are obtained from the truth table which make their functions true – represents corresponding minterms that makes the function true

## Slide 21: Design Procedure: Example…
Two level logic diagrams of each output variables can be produced directly from their respective simplified expression in SOP forms
    But with multiple-output system, these expressions can be manipulated algebraically further to obtain flexibility of common gates
      Here, gate implementation might require three or more level of gates
Notes: It is performed to employ less number of gates including inverters of the input variables. Moreover, only two input gates are used here which is not practiced in two level implementation
Here (C+D) is used over more than one expression. So it could be implemented only once. For multiple outputs.

## Slide 22: Design Procedure: Example – Logic Diagram

## Slide 23: Binary Adder
Addition – most common and basic arithmetic operation two binary digits
    Four possible operations: 0+0=0, 0+1=1, 1+0=1, and 1+1=10
    Carry is produced in fourth operation which may be propagated to the next significant digits
Half Adder – a combinational circuit that performs addition of two bits
Full Adder – a combinational circuit that performs addition of three bits (i.e. two significant bits and a previous carry)
  Two half adders can be employed to implement a full adder

## Slide 24: Half Adder
Two binary input bits (augend and addend) and two binary output bits (sum and carry)
    Two input and two output variables
Assignment of symbols – two inputs [x & y] and two outputs [S & C]
    S represents the LSB and C represents the MSB of the sum
Truth table to identify the function of the half adder:

## Slide 25: Half Adder – Function and Circuit
Simplified Boolean functions for two outputs:
  These functions could be implemented in different ways as well.
Circuit implementation of half adder:
Notes: To be noted :
  De Morgan’s Law:
To be noted :
  𝐱⊕𝒚=(𝒙+𝒚)(𝒙^′+𝒚′)
  𝐱⊙𝒚=𝒙𝒚+𝒙^′ 𝒚′
  De Morgan’s Law: (𝐱+𝒚)′=𝒙^′ 𝒚′

## Slide 26: Full Adder
For addition of n-bit binary numbers, it requires the use of a full adder
  Bit by bit addition will be occurred beginning from the LSB
A full adder is a combinational circuit that performs the arithmetic sum of three input bits
Three inputs (x, y and z) and two outputs (S and C)
    x and y are two significant bits to be added
    z represents the carry from the previous lower significant position
    Two outputs are necessary because the arithmetic sum of three binary digits ranges in value from 0 to 3
    S is the LSB of the sum and C is the MSB

## Slide 27: Full Adder – Truth table and K-map

## Slide 28: Full Adder – Implementation in SOP form

## Slide 29: Full Adder – Implementation with Half Adder

## Slide 30: Binary Adder Binary Ripple Carry Adder
Binary adder – a digital circuit that produces the arithmetic sum of two binary numbers of n number of bits
    It requires a chain of n full adders or a chain of one half adder and (n – 1) full adders in cascade.
      Subscript 0 denotes the LSB and (n-1) denotes the MSB
      The input carry C0 in the least significant position of the first case must be 0.
    Output carry of any full adder is connected to the input carry of the next full adder in the chain
    Example: A=1011 and B=0011 will produce the sum, S=1110 with four bit adder as follows:
Notes: Ripple carry adder: The input carry to the adder is C0 and it ripples (flows) through the full adders to the output carry C4

## Slide 31: Binary Adder Binary Ripple Carry Adder
If we follow the classical method, it would require a truth table with 29=512 entries
  By using an iterative method of cascading a standard function, it is possible to obtain a simple and straightforward implementation.
  All the carries must be generated to obtain correct sum at the outputs.

## Slide 32: Carry Propagation
As any combinational circuit, the signal must be propagated through the gates before the correct outputs are present in the output terminals
Any combinational circuit will always have some value at its outputs
  These outputs will not be correct unless the enough propagation delay is maintained
This propagation delay is crucial if a system uses this type of adder successively
  Solution:
    Faster gates in this circuit – but impractical
    Complex circuit – carry lookahead logic

## Slide 33: Carry Propagation with Full Adder
Notes: Here, subscript i denotes a typical stage
From the input carry Ci to output carry Ci+1, carry, signal propagates through 2 gates
  For n-bit adder, there will be 2n gate levels for carry propagation
G = carry generator, it generates the carry for sure
P = carry propagate, Not sure, but it determines if a carry will propagate or not in the next stage

## Slide 34: Carry Propagation with 4-bit Full Adder To generate Carry Lookahead
+

## Slide 35: Carry Lookahead Generator Circuit For 4-bit Adder
Notes: Now, C3 doesn’t need to wait for C2 and C1 being propagated to generate the its output.
  This gain is achieved at the expense of complex circuit

## Slide 36: 4-bit Binary Adder with Carry Lookahead
Notes: Si= Pi xor Ci

## Slide 37: Binary Subtractor
The subtraction of two unsigned binary numbers – taking the complement of the subtrahend and adding it to the minuend
  Complement of a number can be obtained by 1’s or 2’s complement
So subtraction is a kind of addition operation – needs full adder for machine implementation
If the minuend bit is smaller than the subtrahend bit, a 1 is borrowed from the next significant position – also must be conveyed to the next higher pair of bits by means of a binary signal from current stage to next higher stage
Notes: 1’s complement is easy to implement using inverters.

## Slide 38: Binary Subtractor…
Two kind of subtractor based on the number of inputs:
  Half-subtractor
  Full subtractor
For signed-complement system, addition and subtraction could be implemented using same circuit like unsigned number system.
  Users should interpret the system wisely considering it is signed or unsigned number
  So same circuit could be used to handle both types of arithmetic

## Slide 39: Half-Subtractor
A combinational circuit – subtracts two bits and produces their differences and an output that specifies if a 1 is borrowed or not to next stage.
Designation of the input variables – minuend (x) and subtrahend (y)
D = 2B + x – y, [if x<y, B=1]

## Slide 40: Half-Subtractor…
Boolean functions of two outputs of the half-subtractor:
Logic for D is same as the logic for S in half-adder
Circuit Implementation of half-subtractor:

## Slide 41: Full-Subtractor
A combinational circuit – performs a subtraction between two bits considering the previous borrow – three inputs and two outputs
Designation of variables – inputs [minuend(x), subtrahend(y), previous borrow(z)] and outputs [difference(D) and current borrow (B)]
Considering , if z=0, it will be same as half-subtractor
  If , B=1

## Slide 42: Full-Subtractor…
Truth table of the full-subtractor:
K-map for full-subtractor to simplify:

## Slide 43: Full-Subtractor…
The simplified Boolean function of full-subtractor:
z
The output of B resembles the function for C in the full adder – except x is complemented
The output of D is exactly same as the output S in the full adder
Because of these similarities, it is possible to convert a full adder into a full subtractor - ???

## Slide 44: Full-Subtractor with Half-Subtractors

## Slide 45: 4-bit Full Adder-Subtractor
Notes: If M = 0, this circuit works as adder, other wise subtractor using 2’s complement

## Slide 46: Overflow
When two numbers with n digits each are added and the sum is a number occupying n + 1 digits
  Problem in digital computers, as there is a finite number of bits
    Overflow detection is required to handle this occurrence
  Not possible with paper and pencil as there is no limit of space
Only happens during addition, but not for subtraction
  When both numbers are either positive or negative
Also depends on the types of numbers:
  Unsigned numbers:
    Overflow detected by end carry of the MSB
  Signed numbers :
    A range is maintained from max positive to min negative. If the sum crosses the range, an overflow occurs
      (n+1)th bit indicates the sign bit of the result
    Note: Sign bit is treated as a part of a number and carry doesn’t indicate an overflow

## Slide 47: Overflow - Example
Note that the eight-bit result that should have been positive has a negative sign bit (i.e., the eighth bit) and the eight-bit result that should have been negative has a positive sign bit. As 9-bit storage is not possible, an overflow has occurred.
Overflow condition: carry in and out in the MSB position is not same. (Try +70 and +50 to check overflow)

## Slide 48: BCD Adder

## Slide 49: BCD Adder – Block Diagram

## Slide 50: Binary Multiplier
Multiplication in binary is performed in the same way as multiplication in decimal
  Multiplicand is multiplied by the each bit of the multiplier starting from the LSB
    Each such multiplication forms a partial product
    Successive partial products are shifted one position to the left
    Final product is obtained from the sum of the partial products
  Example: If A, B and C are binary variables:

## Slide 51: Two Bit Binary Multiplier
Note: Multiplier with more bits can be constructed in a similar fashion
Notes: LSB of the result (product) is directly produced by the first AND gate (i.e. A0B0)

## Slide 52: Binary Multiplier – Important
The number of partial products (levels of AND gates) is same as the number of bits in the multiplier
J multiplier bits and K multiplicand bits will require in multiplication:
    AND gates
    K-bit adders
  to produce a product of bits

## Slide 53: Example – Binary Multiplier
Example:
shifted
shifted

## Slide 54: Binary Magnitude Comparator
Comparison operation determines between two numbers whether one number is greater than, less than or equal to the other number
Binary magnitude comparator:
    A combinational circuit that compares two binary numbers A and B
    Outcome of the comparison is specified by three binary variables that indicate whether
Note: If ordinary design procedure is followed, for two n-bit numbers, the truth table will have 22n entries
    Too cumbersome to handle
    Example: with n=3, the truth table will have 64 rows
  Rather a pattern is followed (an algorithm) to solve this problem
    Some patterns occurs frequently which makes it easy build a simple combinational circuit.

## Slide 55: Four Bit Magnitude Comparator
Comparator with single bit:
  If A>B
  If A=B
  If A<B
Comparator with Four bits:
  Try the above methods four times and add them up
Expressions:

## Slide 56: Four Bit Magnitude Comparator Circuit

## Slide 57: Encoder-Decoder
Normally, any discrete information can be represented in binary code
  Here, a n-bit binary code can represent 2n different elements
Encoders convert 2n unique lines of input into a code of n bits and Decoders decode the n bits into 2n unique lines.

## Slide 58: Decoder
For a decoder, if it has unused combinations for a n-bit code, it will produce the output lines less than 2n
Representation of a decoder: n-to-m line decoder
  Where
Usage of decoder:
  To generate the 2n (or fewer) minterms of n input variables
  Moreover, this circuit could be used for code conversion (e.g. binary to octal)

## Slide 59: 3x8 Decoder: as a Binary to Octal Converter
Notes: For each possible input combination, there are seven outputs that are equal to 0 and only one that is equal to 1 in the truth table

## Slide 60: Decoder with NAND Gate and Enable Input
Some decoders are constructed with NAND gates to make it more economical
  In this case, minterms are generated in the complemented form
  Similarly, the operation of the decoder can be controlled with 0s instead of 1s.
Some of them can include one or more enable inputs to control the circuit operations
  Variants: Active-low and active-high enable
Notes: Home task: Decoder with NOR gates and Enable input for Five input variables (15 marks – first 10, 10 marks – next 10)

## Slide 61: Decoder with NAND gates and Enable Input (E)
0 is considered “enable” for both inputs and E because of NAND gate
Specialty with “X” in inputs condense the truth table
Notes: Home task: Decoder with NOR and OR gates and Enable input for Five input variables (15 marks – first 10, 10 marks – next 10)

## Slide 62: Demultiplexer with Decoder
Discussed later on in this chapter
  At first we have to know about multiplexer

## Slide 63: Larger Decoder with Smaller Ones
4x16 decoder with two 3x8 decoders:
Notes: In general, enable inputs are a convenient feature for interconnecting two or more standard components for the purpose of combining them into a similar function with more inputs and outputs.

## Slide 64: Significance of Enable Input
In general, enable inputs are a convenient feature for interconnecting two or more standard components for the purpose of combining them into a similar function with more inputs and outputs.

## Slide 65: Combinational Circuit with Decoders
We consider the minterms of any function from the truth table of certain Boolean function and add them with an external OR gate for each output variable
Example: Full Adder with 3x8 decoder

## Slide 66: Combinational Circuit with Decoders…
If the number of minterms (k) is so many (>2n/2) we can consider the F’ with (2n-k) number of minterms
  Then NOR gate will be used instead of OR gate
If the internal gate of the Decoder is NAND gate, the external gate will be also a NAND gate instead of an OR gate
  Two level NAND gate implementation
Notes: Home task: Implement the Full adder with a Decoder where two level NOR gate implementation is maintained (10 marks – first 10, 5 marks – next 10)

## Slide 67: Encoder
Inverse of Decoder
2n inputs and n outputs
  Only one input will be 1 at a time
Another kind of converter or coder or cryptographer

## Slide 68: 8x3 Encoder: Truth Table and Circuit
Octal to Binary Encoder

## Slide 69: Problems: Ambiguity
If there are 1s in more than one inputs, output could be undefined
  Solution: Priority encoder to ensure the input priority
0 for two different representations – (i) when all the inputs are 0 and (ii) D0 = 1
  Solution: Add another output to observe

## Slide 70: Priority Encoder with additional Output
It includes the priority function for the inputs
Truth table and K-map:
Notes: V is for valid bit = this is a valid bit indicator that is set to 1 when one or more inputs are equal to 1. If all inputs are 0, there is no valid input and V is equal to 0.

## Slide 71: Priority Encoder with additional Output…
Circuit:

## Slide 72: Multiplexer
Also called as data selector
A combinational circuit:
  Selects from one of many input lines and directs it to a single output line
    Selection is controlled by a set of selection lines
  There are 2n input lines and n selection lines
Often labeled as MUX
Notes: Wedge shaped symbol which has one thick edge and narrowed down to one thin edge

## Slide 73: 4-to-1 MUX

## Slide 74: Multiplexer from Decoder
The AND gates and inverters in the multiplexer resemble a decoder circuit
  Indeed, they decode the selection input lines
  In general, a 2n-to-1-line multiplexer is constructed from an n-to-2n decoder by adding 2n input lines to it, one to each AND gate.
    The outputs of the AND gates are applied to a single OR gate.

## Slide 75: Circuit Implementation with Multiplexer
Multiplexer circuits (more than one) can be combined with common selection inputs to provide multiple-bit selection logic for all of them.

## Slide 76: Circuit Implementation with Multiplexer Normal way
The individual minterms can be selected by the data inputs of the multiplexer
  Implement a Boolean function of n variables with a multiplexer that has n selection inputs and 2n data inputs – one for each minterm.

## Slide 77: Circuit Implementation with Multiplexer More efficient way (Example 1)

## Slide 78: Circuit Implementation with Multiplexer More efficient way (Example 2)

## Slide 79: Demultiplexer
Also called as data distributor
Definition: A circuit that receives information from a single line and directs it to one of 2n possible output lines
Selection of a specific output will be controlled by bit combination of n selection lines
A decoder could be used as a demultiplexer
  Here, the enable input in decoder works as the original input in demultiplexer
    Connected with each of the outputs , but only one will be activated specified by the binary combination of the input bits of the decoder
  Decoder with enable input referred as a decoder-demultiplexer

## Slide 80: Demultiplexer: Symbol and Circuit
Notes: Semiconductor: a material having conductivity falling between conductor and insulator. Basis of any IC

## Slide 81: Three State Gates
In digital electronics, three-state logic, tri-state logic, or 3-state logic allows an output or input pin to be in a high impedance state (additional), which means effectively removing that output or input from the circuit.
  This is in addition to the 0 and 1 logic levels that are used in digital electronics.
  Sometimes denoted as Hi-Z
Tri-state gates have additional circuitry via which the gate outputs can be enabled or disabled.
This allows multiple circuits to share the same output line or lines
  Such as a communication bus which cannot listen to more than one device at a time but they are connected all together with tri-states.
Sometimes, they are implemented with conventional logic like AND or NAND
  But most commonly used with buffer gate

## Slide 82: Tri-state Buffer - Symbol
A normal buffer with additional control line entering the bottom/top of the symbol
  This tri-state buffer has a normal input, an output and a control input which determines the state of the output
    When the control input is 1, the output is enabled and the buffer gate behaves like a conventional buffer.
    When the control input is 0, the output is disabled and the gate goes to a high-impedance (Hi-Z) state.
  Because of this feature, a large number of tri-state gate outputs are connected with wires to form a common line without endangering the loading effects

## Slide 83: Tri-state gate – More gates
Notes: buf means buffer controlled by 0 or 1
not means buffer controlled by 0 or 1

## Slide 84: Consequence of a High Impedance State (Hi-Z)
The third state is a high-impedance state (Hi-Z) in which
  The logic behaves like an open circuit
    Which means that the output appears to be disconnected
  The circuit has no logic significance
  The circuit connected to the output of the three-state gate is not affected by the inputs to the tri-state gate.

## Slide 85: Multiplexer with Tri-state Buffer
Note: Outputs are connected together to form a single output line.
Also, if enable input of the tri-state is 0, all the outputs are 0 and bus line is in a Hi-Z state

## Slide 86: abc

## Slide 87: abc

## Slide 88: NAND Implementation: Analysis Procedure
Reverse process – starts from given NAND logic diagram and ends with a Boolean expression or truth table
Specialty – Application of De Morgan’s Law
Derivation of Boolean Function from NAND Logic Diagram
  All gates’ outputs are labeled with arbitrary symbols
  The Boolean functions for the outputs of gates that receive only external inputs are derived. It may follow De Morgan’s law to make it convenient to use
  Boolean output functions of gates which have inputs from previously derived functions are determined in consecutive order until the output is expressed in terms of input variables

## Slide 89: NAND Imp.: Analysis Procedure …
Example:

## Slide 90: NAND Imp.: Derivation of Truth Table
Same as before.

## Slide 91: NAND Imp.: Derivation of Truth Table …
Now we can use K-map to get the simplified expression of the given NAND logic circuit.

## Slide 92: NAND Imp.: Block Diagram Transformation
Without employing De Morgan’s Law.
We use two alternate graphic symbols of NAND gates

## Slide 93: NAND Imp.: Block Diagram Transformation…
NAND logic diagram – AND-OR diagram conversion
  A change in symbols from AND-invert to an invert-OR in alternate levels of gates.
  At first we start from the last level, to be changed to an invert-OR symbol.
  These changes produce pairs of circles along the same line – can be removed as they can be cancelled.
  One input AND or OR gate can be changed to an inverter.
  Circle with external input can be changed to corresponding complemented variable.

## Slide 94: NAND Imp.: Block Diagram Transformation…

## Slide 95: Block Diagram Method: NOR Imp.
In general, the number of NOR gates required to implement a function is equal to the number of AND-OR gates, except for an occasional inverter. It will be applicable when both normal and complement inputs are available.

## Slide 96: NOR Implementation: Analysis Procedure
To derive the Boolean function from a logic diagram, we mark the outputs of various gates with arbitrary symbols.
By repetitive substitutions, we obtain the output variables as a function of the input variables.
To obtain the truth table from a logic diagram without deriving the Boolean function first, we form a table listing the n input variables with 2n rows of 1s and 0s. The truth table of various NOR gate outputs is derived in succession until the output truth table is obtained.

## Slide 97: Block Diagram Transformation
To convert a NOR logic diagram to its equivalent AND-OR logic diagram, we use the two symbols for NOR gates.
The conversion of a NOR logic diagram to an AND-OR diagram can be achieved through a change in symbols from OR-invert to invert-AND starting from the last level and in alternative levels.
Pairs of small circles along the same line must be removed.
A one-input AND or OR gate should be removed but if it has a small circle at the input or output, it should be converted to an inverter.

## Slide 98: Block Diagram Transformation