## Slide 1: Sequential Logic
Course Teacher: Md. Hamjajul Ashmafee
Lecturer, CSE, IUT
Email: ashmafee@iut-dhaka.edu
CSE 4205 Digital Logic Design

## Slide 2: Remaining to Add
Review other books and internet resources
Notes: What is digital computer? Examples where we can use this thing.

## Slide 3: Introduction – Combinational Circuit
So far digital circuits considered earlier – combinational circuit
  But, it is only a part of the digital system.
Definition:
  Output at any instant entirely depends on the current inputs .
  If there is any change in the inputs, the output will be changed immediately (considering the propagation delay)
Example: Adder

## Slide 4: Introduction – Memory
Electronic devices nowadays have the ability to send, receive, store, retrieve and process information in binary format
  It is only possible because of ability to store information (memory)
The circuits that include memory element called sequential circuit/logic
  It is another major aspect of the digital system
But, design of sequential circuit depends on the combinational circuit design

## Slide 5: Sequential Circuit
Storage elements stores binary information (1 or 0) which are called states
  This states are time variant
Present output of the sequential circuit = F1 (present input, present state)
Next state of memory element = F2 (present input, present state)
Storage element feeds back its state as input to the combinational circuit through a feedback path
  This feedback path is called a loop
Example: Counter, Register

## Slide 6: Sequential Circuit – A closer Look

## Slide 7: Time Sequence
Sequential circuit includes time sequence of inputs, outputs and internal memory states
  This time-sequence determines the behavior of a sequential circuit.
Notes: Here, S and R are inputs
Y is output
Q is the present memory state

## Slide 8: Classification of Sequential Circuit
Two types of sequential circuit – based on timing of their input signal
  Synchronous or clocked sequential circuit
  Asynchronous or unclocked sequential circuit

## Slide 9: Asynchronous Sequential Circuit
  Behavior defined based on the order/sequence of input signals at any instant of time
    Only affected whenever the inputs change
    No synchronization with clock pulse
  Example: Latch
  Time delayed memory element
    Propagation delay is kept higher to provide storage attributes
    Intentionally built with delay units
  Drawback: unstable states at times due to some undesirable feedbacks
  Advantage: faster than the synchronous sequential circuit

## Slide 10: Synchronous Sequential Circuit
  Behavior defined based on the input signals at discrete instants of time
  Example: Flip-flop
  Synchronization achieved through timing device
    Also, known as system clock or master clock generator
    It generates a periodic train of clock pulses
    This clock pulse is ANDed with specific input signal
  Clock pulse driven storage element
    Only affected with arrival of each clock pulse
  Clock pulse will define when changes will occur
  External inputs will define what changes will occur
  Advantages – eliminate instability problem
  Common practice in electronic devises

## Slide 11: Clocked Sequential Circuit
Note: Here, the storage element is a flip-flop

## Slide 12: Clock
Tw = pulse duration

## Slide 13: Flip-flops
Memory elements in clocked sequential circuit
A binary/digital memory cell that stores one bit of information
Number of inputs – One or more
Two outputs – normal (Q) and complement (Q’) value of the bit stored
  Q=1, Q’=0 : set (1) state and Q=0, Q’=1 : reset (0) state
  Q and Q’ can’t be same state at a time
  If it happens, it goes to undefined state
Also known as a bistable multivibrator
Notes: Bistable = stable in either states (0 and 1)
Multivibrator = an electronic circuit which is used to implement a simple two state system

## Slide 14: Flip-flops…
Block diagram of a flip-flop
Bistable Multivibrator Circuit

## Slide 15: Flip-flops…
Implemented with NAND or NOR gates
Differences in types of flip-flops:
  Based on number of inputs and the manner in which the inputs affect the binary state
Edge triggered device

## Slide 16: Latch
It has two stable states
Used to store binary information
  Binary memory element
Latches are basic storage elements that operate with signal levels (rather than signal transitions).
  Level triggered device
It is not synchronized with clock pulses

## Slide 17: Latch vs Flip-flop
The state of flip-flop changes at active state of clock pulses and remains unaffected when the clock pulse is not active.
  It serves as a memory element in synchronous sequential circuits
  It is applied with clock pulses
In particular, the unclocked flip-flops (i.e., latches) changes its states of the output immediately based on the applied input
  It serves as memory elements in asynchronous sequential circuits.
  Sometimes it is applied enable input

## Slide 18: Types of Flip-flops
Based on how the inputs and clock pulses cause transition between two states:
  S-R (Set-Reset) flip-flop
  D (Data) flip-flop
  J-K (J: set, K: reset) flip-flop
  T (Toggle) flip-flop

## Slide 19: S-R (Set-Reset) flip-flop
Two inputs – Set (S) and Reset (R)
Two outputs – Q and Q’ (complement to each other)
Made of cross-coupled connection from output to input constituting a feedback path

## Slide 20: S-R (Set-Reset) Latch – with NOR Gates Level triggered device
Not clocked or synchronized
  Level triggered
  Asynchronous sequential circuit
Note: The output of a NOR gate is zero (0) if any of the inputs are 1, irrespective of the other input.
(after an undefined occurrence)
(Set state)
(Reset state)
(Memory state)
Notes: Discuss all cases from the truth table
  Start with S=0 and R=0. It considers both cases of Q (0 and 1). It results in memory state
  Then, S=0 and S=1 (second and third cases). Here we will not consider Q. Because, inputs themselves force to change the Q.
S (input) and Q (output) should be in opposite direction/level for with NOR gates
Last occurrence from the truth table is only possible, if its previous state was undefined. After that if the state is S=0 and R=0, the output, Q totally depends on speed of the NOR gate (which NOR gate will be 0 at first)

## Slide 21: S’-R’ Latch – with NAND Gates Level triggered device
Also, not clocked or synchronized
  Level triggered and asynchronous sequential circuit
  Operationally similar as NOR based S-R flip-flop
Note: The output of a NAND gate is one (1) if any of the inputs are 0, irrespective of the other input.
(after an undefined state)
(Set state)
(Reset state)
(Memory state)
Notes: It is called S’-R’ because, S’ and R’ with NAND gates is similar to S and R with NOR gates. It can be verified from the truth table mentioned above.
But, they, both are same in operation with S and R inputs which can be justified from the truth table
Discuss all cases from the truth table
S (input) and Q (output) should be in same direction/level for with NAND gates
Last occurrence from the truth table is only possible, if its previous state was undefined. After that if the state is S=0 and R=0, the output, Q totally depends on speed of the NAND gate (which NAND gate will be 1 at first)

## Slide 22: Comparing S-R and S’-R’ Latch
They just operate in a complement fashion of each other
To convert a NAND-based S’-R’ latch to NOR-based S-R latch, an inverter at each input of the latch should be placed
  This change will make the truth tables and circuits similar
Notes: It is called S’-R’ because, S’ and R’ with NAND gates is similar to S and R with NOR gates. It can be verified from the truth table mentioned above.
But, they, both are same in operation with S and R inputs

## Slide 23: Clocked S-R Flip-Flop
Synchronous circuit
  Activated during a clock pulse is present
From a latch, a flip-flop can be produced including an additional input to control the behavior of the circuit
latch
Notes: If clock=0, both AND gates produce 0 and 0 in the inputs of S and R which in turn keeps the latch in memory state
If the clock=1, the changes in S and R will be passed and change the Q (output).
S and Q should be in opposite direction/level for with NOR gates

## Slide 24: Clocked S’-R’ Flip-Flop
Constructed with NAND gates
S’-R’ latch
S-R Flip-Flop
Notes: If clock=0, both NAND gates produce 1 and 1 in the inputs of S and R which in turn keeps the latch in memory state
If the clock=1, the changes in S and R will be passed and change the Q (output).
This complete circuit works as a S- R flip-flop considering same inputs for S and R

## Slide 25: S-R Flip-Flop [Final version]
Logic symbol and truth table
Three inputs – S, R and CLK
  The clock input is marked with a triangle denoting edge triggered flip-flop
Qn denotes output at nth time and Qn+1 denotes output at (n+1)th time

## Slide 26: Characteristic Table and Truth Table
Characteristic table and truth table:
  Truth table with present input(s) and present state(s) as input column and next state(s) as output column refers to a characteristic table
  It refers to the operational characteristics of the flip-flop

## Slide 27: S-R Flip-Flop - Characteristic table
Characteristic table and Characteristic equation of S-R flip flop
  From book [page 224-225]

## Slide 28: Preset and Clear Inputs
Initially, a circuit is uncertain with Q and Q’ states
They should be assigned with either set or reset state with direct or asynchronous inputs
  Also, called as overriding inputs
  These inputs are individually named as preset (Pr) and clear (Cr)
These inputs are not synchronized with clock
  They can be applied at any time
  CLK = 0 or 1, doesn’t care at all [but, preferred to be applied when clock is inactive]
Pr=0 and Cr=0 must not be applied, as it leads to an uncertain state
Pr and Cr inputs are used with bubbles considering them active low

## Slide 29: Preset and Clear Inputs…
More from book [page 223-224]
  Preset and clear inputs with S-R flip-flop
  Block diagram of an S-R flip-flop with preset and clear inputs
  Truth table with preset and clear inputs

## Slide 30: D Flip-Flop From Book [page 225-227]
Derivation from S-R flip-flop
Truth table and all cases of D flip-flop
Block diagram of D flip-flop
D flip-flop with Pr and Cr inputs
Characteristic table and equation of D flip-flop

## Slide 31: J-K Flip-Flop
Very similar to an S-R flip-flop
  J and K behave like inputs S and R to set and reset the flip-flop
Only difference is eliminating the undefined condition of an S-R flip-flop
  When J=K=1, the flip-flop is said to be in a toggle state
  Toggling means complementing the state in each clock pulse

## Slide 32: J-K Flip-Flop – Implementation
Implementation from S-R flip flop
  Another level of feedback path is included
  Inputs J and K of J-K flip-flop are ANDed with Q’ and Q respectively to obtain the inputs, S and R for S-R flip-flop

## Slide 33: J-K Flip-Flop – Implementation…
Circuit diagram and block diagram of a J-K flip flop with NAND gates
Same circuit diagram in different orientation

## Slide 34: J-K Flip-Flop – Truth Table
Truth table of J-K flip-flop – From book [page-230]
  J-K inputs with S-R inputs of S-R flip-flop to derive the next state
    It is assumed that inputs will not be changed any more during a clock pulse
  Concise truth table (final version) for J-K flip-flop

## Slide 35: J-K Flip-Flop – Characteristic Table
Characteristic table and characteristic equation for J-K flip-flop
  More from book [page 231]

## Slide 36: J-K Flip-Flop – Race Around Condition
Assumption for basic J-K flip-flop:
  The inputs will not be changed any more during a clock pulse
  But, it is not true because of the feedback connections
Consider the scenario: J=K=1
    If Q=1, after △t time, it will be Q=0
    Next, if Q=0, after another △t time, it will be Q=1
  So, basically, during tp time, the output Q will oscillate between 0 and 1
  And, after tp time, the output Q is not certain.
  This situation is called “Race-Around Condition”
△t = propagation delay
tp = pulse duration

## Slide 37: Race Around Condition – Solutions
If △t is in nanoseconds and tp in microseconds, output will be changed thousands of times within a clock pulse
  If tp < △t < T, this race around condition could be avoided
  But, this small propagation delay is very difficult to achieve due to hardware limitation
Master-Slave (M-S) flip-flop
Edge triggered flip-flop

## Slide 38: Race Around Condition – Master-Slave J-K Flip-Flop
A system of two flip-flops – master and slave flip-flops
A clock pulse is applied to master and the inverted form of the same clock is applied to the slave
How to solve RAC problem?
  When CLK=1, gates 5 and 6 will not respond. Output Q and Q’ will only change when CLK=0.
K

## Slide 39: Master-Slave J-K Flip-Flop…
  When CLK=1, the master is enabled. Qm output will respond the inputs J and K
    Slave is disabled
  When CLK=0, the slave is enabled. Q output will respond the outputs Qm and Q’m
    Master is disabled
K

## Slide 40: Master-Slave Flip-Flop – More
The system of M-S flip-flop is not restricted to J-K M-S flip-flop only
  Also, S-R and D M-S flip-flops are possible
  In all of these cases, the slave is an S-R flip-flop whereas the master changes to J-K, S-R or D flip-flops

## Slide 41: Race Around Condition – Edge Triggered Flip-Flop
The circuit has only single chance to accept inputs (e.g., J and K)
  During:
    Negative transition of the clock pulse – negative edge triggered J-K flip-flop
      Outputs are same M-S flip-flop
    Positive transition of the clock pulse – positive edge triggered J-K flip-flop

## Slide 42: T Flip-Flop
A slight modification of the J-K flip-flop
  J and K inputs are tied together – have same input
  Referred as T flip-flop
    It has the ability to toggle
One input (T) and two outputs Q and Q’
Two states – toggle (T=1) and memory (T=0) states
Usage: Counter, switching circuits

## Slide 43: T Flip-Flop From Book [page 233-235]
Truth table of T flip-flop
  Try all cases
T flip-flop with preset and clear inputs
Block diagram of T flip-flop
  Also, from J-K flip-flop
Characteristic table and characteristic equation

## Slide 44: Toggle Mode – S-R flip-flop
Outputs (Q and Q’) are cross-coupled with inputs (S and R)
  Here, S=R=1 is not possible to be applied, as it is an undefined state

## Slide 45: Toggle Mode – D flip-flop
Output Q’ is cross-coupled with input D

## Slide 46: Triggering of Flip-flops
Level Triggering
Edge Triggering

## Slide 47: Excitation Table
A tabulation to figure out all possible input conditions to obtain the desired output condition
  It is required to design a sequential circuit when present state and next state of the flip-flop is specified
    Based on that we need to find out all possible input conditions
    Present and next states are meant the conditions before and after applying the clock pulse respectively

## Slide 48: Excitation Table of all Flip-Flops

## Slide 49: Interconversion of Flip-flops
A conversion logic is required to be designed for such conversions of flip-flops
Steps:
  Produce the characteristic table of the required Flip-flop
  Produce the excitation table of the given Flip-flop
  Combine those tables make a final table including data input(s) of desired flip-flop and Q as the inputs and the input(s) of the given flip-flop as the outputs
Desired

## Slide 50: Interconversion of Flip-flops: Example
Example: From an S-R flip-flop to a D flip-flop
  From Book [page 241-247]
Step 1:
Step 2:
Step 3:

## Slide 51: Interconversion of Flip-flops: Example …
Converted Flip-flop: