## Slide 1: Analysis and Design Procedure of Sequential Circuits
Course Teacher: Md. Hamjajul Ashmafee
Lecturer, CSE, IUT
Email: ashmafee@iut-dhaka.edu
CSE 4205 Digital Logic Design

## Slide 2: Remaining to Add
For Design and Analysis Procedure
  Review other books and internet resources
  Give 2 hours to make it complete and beautiful
For Pattern/Sequence detector:
  Review other books and internet resources
  Draw the figure with Wacom (slide 11)

## Slide 3: Analysis Procedure From book [Page 250]
Starting with a sequential Circuit
Deriving its state table
  2 variants to represent
Deriving its state diagram from the state table
Deriving its state equation from the state table
  Final outcome
  Also, need to describe the behavior of the circuit [Preferred]
Summarize all generalized steps

## Slide 4: Design Procedure From book [Page 254]
Mention all Generalized Steps
Example following those steps

## Slide 5: Example of Design Procedure Sequence/Pattern Detector

## Slide 6: Sequence/Pattern Detector
A sequential circuit that takes the input of binary bit streams and generate an output true (e.g. logic 1) when the target sequence is detected
  Bit stream (1s and 0s) will be fed/inserted as input to check for particular pattern or sequence
    As soon as, the target pattern is detected, it will make the output high
As the output depends on the current state as well as the external input (x), a Mealy FSM is considered

## Slide 7: Sequence/Pattern Detector: Types
Types:
  Overlapping
    The last bit of one sequence becomes the intermediate bit of the next sequence
  Non-overlapping
    The last bit of one sequence doesn’t become the intermediate bit of the next sequence
They will be clear from the examples

## Slide 8: Design A Sequence Detector
Steps:
  Step 1: Develop the state diagram
  Step 2: Perform the state assignment and state reduction
  Step 3: Select the number and type of the flip flop
  Step 4: Derive Circuit Excitation Table
  Step 5: Derive the expressions for input of the flip flops and output(s)
  Step 6: Develop the circuit

## Slide 9: Non-overlapping ‘101’ Mealy Sequence Detector
Example:
State Diagram:
Input : | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1
Output: | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0

## Slide 10: Non-overlapping ‘101’ Mealy SD…
State Assignment:
a | 00 | Nothing detected
b | 10 | ‘1’ detected
c | 01 | ‘10’ detected
Notes: Review: One hot assignment

## Slide 11: Non-overlapping ‘101’ Mealy SD…
Type and number of flip flops:
  Two D flip flops
Circuit Excitation Table:

## Slide 12: Non-overlapping ‘101’ Mealy SD…
Expression Derivation:

## Slide 13: Non-overlapping ‘101’ Mealy SD…
Circuit Implementation:

## Slide 14: Overlapping 101 Mealy Sequence Detector
Example:
State Diagram:
Input : | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1
Output: | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0

## Slide 15: Overlapping 101 Mealy SD…
Others steps would be same as before.

## Slide 16: Administration
abc

## Slide 17: Administration
abc

## Slide 18: Administration
abc

## Slide 19: Administration
abc

## Slide 20: Administration
abc

## Slide 21: Administration
abc

## Slide 22: Administration
abc

## Slide 23: Motivation
abc
Notes: Semiconductor: a material having conductivity falling between conductor and insulator. Basis of any IC